## Slide 1
Product Development Lab – II (24ME411)
Topic : A LOW-POWER SMART SOLDIER HEALTH MONITORING SYSTEM USING LoRa COMMUNICATION
R.M.K. ENGINEERING COLLEGE (AN AUTONOMOUS INSTITUTION) Department of Electronics and Communication Engineering
Team Name : Soldier Safety Research Group (SSRG)
Mentor: Dr. Vijayalakshmi S, M.E, Ph.D, Professor
Team members :
SESHASAAI MA (Team leader) - 111724104084
BALA MANIKANTA K - 111724104068
KAMALESHWARAN M - 111724104069

## Slide 2: OBJECTIVE
To design and develop a low-cost, low-power smart soldier safety and health monitoring system capable of operating in remote and border regions without internet connectivity.
To track soldier location using GPS during emergency situations.
To detect abnormal inactivity or motion using a motion sensor.
To predict health risk prediction using simple ML model (Edge-Based Decision Tree).
To analyze multiple sensor inputs locally using edge processing to reduce false alerts.
To implement LoRa-based communication for long-range, low-power data transmission.
To minimize battery consumption by transmitting data only during abnormal or emergency conditions. To monitor vital health parameters such as heart rate in real time.
To develop a cost-effective prototype under ₹5,000 suitable for academic and field-level research
Primary Objective
Secondary Objectives

## Slide 3: PROPOSED SYSTEM OVERVIEW
Continuous heart rate monitoring
Motion & inactivity detection
GPS-based emergency location tracking
Temperature & humidity monitoring
Event-based alert transmission
Long-range LoRa communication (5–10 km)
Low power consumption
A wearable embedded system that monitors:
Environmental conditions
Performs edge-based decision making
Sends alerts via LoRa only during emergencies
Reduces false alarms and power consumption
SYSTEM FEATURES
Heart rate
Motion / inactivity
SDG

## Slide 4: WHY NOT GSM?
HEART RATE VARIATION HANDLING
Heart rate varies due to:
Individual differences
Temperature
Stress
Vulnerable to:
Jamming
No-signal border regions
GSM requires:
Licensed spectrum
SIM subscription
Network availability
LoRa advantages:
No SIM
No internet
Free ISM band
Secure & reliable
Solution:
Heart rate + Temperature + Humidity correlation
Threshold ranges instead of fixed values
Panic / abnormal condition detected when:
HR abnormal + high temperature OR
HR abnormal + inactivity

## Slide 5: MOTION VS LOCATION
EDGE-BASED DECISION TREE (SIMPLE ML)
Input:
Heart rate
Motion status
Temperature
Time duration
Motion Sensor:
Detects movement patterns
Identifies inactivity, falls, unconsciousness
GPS:
Shows where soldier is
Cannot detect state
Soldier standing guard ≠ inactivity:
Micro-movements detected
Alert only if prolonged abnormal inactivity
Output:
Normal
Warning
Emergency
Uses rule-based Decision Tree
Runs fully on ESP32
No cloud or heavy ML required

## Slide 6: WHAT IF SOLDIER IS IN REST STATE/SLEEPING?
Sleeping soldier:
  Normal heart rate
  Minimal movement
Solution:
  Alert triggered only if:
    No motion + abnormal HR
    No motion beyond allowed guard time
    Manual panic switch not used
Prevents false alerts during resting periods.
WHY THIS IS UNIQUE
Sensors are not unique
Innovation lies in:
  Edge-based intelligence
  Event-driven communication
  LoRa-based decentralization
Focus on power, cost, reliability, and context

## Slide 7
LIST OF COMPONENTS
S.NO | COMPONENT | PURPOSE | COST (INR)
1. | ESP32 WROOM-32C Microcontroller | Processing & control | 589
2. | MAX30102 (Heart Rate + SpO2) | Health monitoring | 299
3. | MPU6050 (6-Axis Gyro + Accelerometer) | Motion detection | 280
4. | NEO-6M GPS Module | Location tracking | 379
5. | LoRa SX1278 (for long range) | Communication | 589
6. | DHT22 (Temp & Humidity) | Environment | 219
7. | Li-po Battery, Wires, Switch | Power & Misc | 800
Total Cost ≈ ₹3,100

## Slide 8: IMPLEMENTATION OF PROJECT
The proposed system is designed as a compact, body-worn unit to ensure minimal interference with soldier mobility and field operations.
The central processing unit (ESP32), LoRa module, and battery are enclosed in a small rugged casing
The unit is worn:
  On the chest strap, shoulder vest, or waist belt
  Similar to existing military communication devices
This ensures:
Stability during movement
Protection from environmental exposure
Ease of maintenance and replacement
Wearable Deployment Design
S.NO | COMPONENT | PLACEMENT | REASON
1. | Heart Rate / SpO₂ (MAX30102) | Finger or wrist strap | Accurate pulse & oxygen saturation
2. | Temperature and Humidity sensor(DHT 22) | Near skin surface (chest/arm) | Reflects body temperature trends
3. | Motion sensor(MPU6050) | Inside main module (chest/waist) | Detects posture, inactivity, impact
4. | GPS Module | Top-facing module | Clear sky visibility
5. | LoRa SX1278 Antenna Module | External and elevated position | Long-range communication reliability
Sensor Placement on Soldier Body

## Slide 9
Soldiers may remain stationary for long durations (2–3 hours) during surveillance
Therefore, no alert is generated solely based on inactivity
Motion data is interpreted contextually using:
  Heart rate trends
  Body temperature variation
  Environmental temperature & humidity
This avoids: ❌ False alerts during guard duty ❌ Misclassification of normal stationary behavior
Edge processing ensures:
No continuous transmission
Reduced power consumption
Lightweight design:
Total device weight kept minimal
Suitable for long-duration deployment
The system identifies abnormal conditions only when multiple parameters simultaneously deviate, such as:
Sudden drop or spike in heart rate
Abnormal temperature rise relative to ambient conditions
Absence of micro-movements (postural change)
Prolonged abnormal physiological state
Only under these combined conditions: ➡ Emergency alert is transmitted via LoRa
Motion & Inactivity Interpretation
Power & Comfort Considerations
Handling Unconscious or Medical Emergency Scenarios

## Slide 10: CURRENT REAL PROBLEM (FIELD REALITY
Soldiers deployed in border and remote regions often operate in areas with:
  Unreliable or unavailable GSM/internet connectivity
Continuous human supervision is not feasible due to:
  Large distance between posts
  Long guard durations (2–4 hours)
Health-related emergencies such as:
  Heat stress
  Sudden fatigue
  Panic-induced abnormal vitals may go undetected for long durations
Existing high-end monitoring solutions are:
  Cost-intensive
  Power-hungry
  Difficult to deploy at scale for all personnel

## Slide 11: SIMPLE ML-BASED HEALTH RISK PREDICTION (EDGE DECISION TREE)
Problem with Single-Parameter Monitoring
Heart rate varies due to:
  Physical activity
  Stress
  Environmental heat/cold
Body Temperature alone does not indicate medical risk
Motion alone cannot distinguish:
  Standing alert
  Resting
  Medical emergency
Proposed Solution
A context-aware Decision Tree running on the ESP32
Combines physiological, environmental, and motion data
Performs local risk assessment at the edge
Input Parameters
Heart Rate (bpm)
Ambient Temperature (°C)
Humidity (%)
Motion Status (Active / Inactive / Sudden fall)
Time duration of inactivity

## Slide 12
Decision Logic (Example Rules)
IF
  Heart Rate ↑
  AND Temperature ↑
  AND Humidity ↑
  AND Motion = Active → Heat stress / Panic risk
IF
  Motion = No movement
  AND Heart Rate abnormal
  AND Time > Threshold → Possible medical emergency
IF
  Motion = No movement
  AND Heart Rate normal → Normal stationary duty (No alert)
Why This Approach is Effective
Reduces false alerts.
Differentiates rest vs emergency.
Adapts to environmental conditions.
Requires no cloud or internet.
Suitable for real-time border deployment
Output States
Normal (No transmission)
Warning (Local monitoring)
Emergency (LoRa alert + GPS location)

## Slide 13
Many existing soldier monitoring solutions are designed for:
High reliability
High accuracy
Such systems often involve:
Complex communication infrastructure
Higher power consumption
Continuous monitoring approaches:
Increase battery usage during long deployments
High-end systems are:
Expensive to deploy for all personnel
More suitable for critical missions than large-scale routine monitoring
To explore a low-power, cost-effective monitoring approach
To reduce unnecessary data transmission using event-based logic
To utilize LoRa communication for remote areas without internet
To combine multiple low-cost sensors for improved context awareness
To design a system suitable for long-duration field operation
PRACTICAL CONSTRAINTS IN EXISTING SYSTEMS
HOW OUR PROJECT ADDRESSES THESE GAPS

## Slide 14: REFERENCE
R. R. Jadhav, P. S. Patil, and S. R. Patil, “Wearable health monitoring system for soldiers using wireless sensor networks,” International Journal of Engineering Research and Technology, vol. 8, no. 4, pp. 227–231, Apr. 2019.
S. Thotakura, S. Movva, L. Apoorva, and J. Susmitha, “LifeLine: Smart soldier health monitoring and situational awareness system powered by ESP8266 and IoT integration,” in Proc. 2025 6th Int. Conf. Electronics and Sustainable Communication Systems (ICESC), Coimbatore, India, Sept. 2025, doi: 10.1109/ICESC65114.2025.11212282.
A. Aggarwal, V. Kumar, V. Singhal, and R. Yadav, “Soldier health and position tracking system,” in Proc. Int. Conf. Sustainable Emerging Innovations in Engineering and Technology (ICSEIET), Ghaziabad, India, Sep. 2023, doi: 10.1109/ICSEIET58677.2023.10303559.
V. Patel, N. Yeware, B. Thombre, and A. Chopde, “Soldiers health monitoring and position tracking system,” in Proc. IEEE Int. Students’ Conf. Electrical, Electronics and Computer Science (SCEECS), Bhopal, India, Feb. 2024, doi: 10.1109/SCEECS61402.2024.10482038.
V. S. Pund, S. K. Dongare, P. S. Amate, D. R. Jadhav, R. R. Bibave, and D. B. Pardeshi, “Soldier health monitoring and position tracking (E-vest),” in Proc. 4th Int. Conf. Electronics and Sustainable Communication Systems (ICESC), Coimbatore, India, Jul. 2023, doi: 10.1109/ICESC57686.2023.10193616.
J. Swetha Priyanka, A. Deshpande, G. Raja Mourya, and A. Kumar, “Soldier safety using GPS and GSM modem,” in Proc. Third Int. Conf. Inventive Research in Computing Applications (ICIRCA), Coimbatore, India, Sep. 2021, doi: 10.1109/ICIRCA51532.2021.9545025.
S. Sharmila Devi, S. Lakshana, S. V. Pavithra, and S. Ruthva Roshini, “LoRa based smart soldier jacket,” in Proc. Second Int. Conf. Augmented Intelligence and Sustainable Systems (ICAISS), Trichy, India, Aug. 2023, doi: 10.1109/ICAISS58487.2023.10250649.
D. G. Fernald, “U.S. Army software system safety process, case-study, and success stories,” in Proc. Annu. Reliability and Maintainability Symp. (RAMS), Palm Springs, CA, USA, Jan. 2020, pp. 1–6, doi: 10.1109/RAMS48030.2020.9153623.
B. Veerasamy, B. Gayathri Durga, T. Harish Muthu Kumaran, Innamuri Venkata Devika, and M. Jeya Akshaya, “Soldier health detection and position tracking system using LoRaWAN sensor for low power and long-range access,” in Proc. 7th Int. Conf. Trends in Electronics and Informatics (ICOEI), Tirunelveli, India, Apr. 2023, pp. 1–6, doi: 10.1109/ICOEI56765.2023.10125644.

## Slide 15: CONCLUSION
A practical and affordable soldier safety system
Combines health, motion, and location monitoring
Uses edge intelligence and LoRa communication
Suitable for real-world deployment scenarios
Encrypted LoRa communication
Personalized health profiles
Solar or kinetic energy harvesting
Base-station dashboard
FUTURE ENHANCEMENTS
“This work focuses on optimizing power consumption and deployment cost, rather than competing with existing high-end military systems.”